Vredestein launches first all-season tyre for ultra-high-performance segment

Apollo Vredestein is set to further strengthen its leading position in the all-season segment in Europe with the launch of a brand-new all-season tyre, the Vredestein Quatrac Pro. This is the first all-season tyre to be specially designed for the ultra-high performance (UHP) segment and cars such as the Alfa Romeo Stelvio, Volvo XC90 and BMW 5-series. The Quatrac Pro will be available in sizes from 17 to 21 inch. Vredestein’s Quatrac 5 will continue to serve as the ideal all-season tyre in the smaller size range.

Benefiting from Vredestein’s 26-plus years of all-season experience, the new Quatrac Pro offers the performance required by UHP cars. The new all-season tyre offers superb handling and short braking distances under both dry and wet conditions and also eliminates the need to switch tyres from season to season for car owners in this segment. The Quatrac Pro guarantees safety even with unexpected weather changes. The new model provides more than 10% better wet grip* and 5% better snow handling*. As with other Vredestein tyres, the Quatrac Pro bears the signature of Italdesign Giugiaro, ensuring a premium appearance that is every bit as impressive as its performance.

Performance-oriented construction and material design

The advanced technology integrated in the Quatrac Pro includes wider longitudinal grooves combined with diverging grooves in the shoulder, optimising water evacuation and improving safety on wet distances even at high speeds. Moreover, wide centre ribs will provide the optimal steering sensitivity and control that is required for cars in the UHP segment.

The advanced compound material has a high silica and resin content, which ensures excellent traction on wet and snowy roads, while the exceptionally even pressure distribution means the sipes in the centre area are very effective on snow. Finally, the distinctive winter and summer sides guarantee high performance in all seasons – the tyre carries the European snowflake symbol, indicating compliance with EU winter tyre regulations (ECE R117).

Unique sizes

The Quatrac Pro goes on sale on the 1 April 2019 and will be available in 50 sizes, 29 of which with the Y-speed rating (speeds up to 300 km/h). Fourteen sizes will be absolutely unique in the all-season segment, including the 315/35 R20 fitted on a BMW X5 (rear wheel).

The introduction of the Quatrac Pro allows Vredestein to take a leading position in the all-season segment, with the most number of sizes available on the European market.

*Data based on internal testing compared to predecessor Quatrac 5 in development size 245/45 R18 100Y XL

For more information please contact:

Tamara Oostveen, Manager PR & Events Europe

T: +31 6 42 37 41 01

E: tamara.oostveen@apollovredestein.com

About Apollo Vredestein

Apollo Vredestein BV designs, manufactures and sells top-quality tyres for passenger cars, two-wheelers and commercial vans, as well as a range of agricultural and industrial tyres, through its locations in Europe and the USA. Apollo Vredestein is part of Apollo Tyres Ltd, an international tyre major with manufacturing units in India, the Netherlands and Hungary. Apollo Tyres Ltd markets products under its two global brands Apollo and Vredestein. The company's products are available in over 100 countries through a vast network of branded, exclusive and multi-product outlets.